## Slide 1: Logic circuits
Terebes Liviu Cristian

## Slide 2: Task
Write a Boolean function of 4 variables given by its table of values, simplify it and draw the logic circuits corresponding to all its simplified forms.

## Slide 3: Simplification procedure
The simplification process used in this case is described as follows:
  1. The function f is transformed into DCF(f)
  2. We place the found minterms (from DCF(f)) in a Veitch diagram
  3. We obtain the set of maximal monoms (M(f)) from the diagram, by applying factorizations as follows: 4-factorization, 3-factorization…0-factorization (in each k-factorization process we try to find a monom which contains the common variables of all 2^k neighbor cells)
  4. We select the set of central monoms (C(f)) from M(f) (if a group of minterms covered by a maximal monom ma contains at least one minterm circled once, then ma∈C(f))
  5. We identify the case of the simplification algorithm and we obtain all the simplified forms of f.

## Slide 4: Simplification algorithm

## Slide 5: The Boolean function and its DCF
a | b | c | d | f(a,b,c,d)
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Remark: The disjunctive canonical form, DCF, is the disjunction of the minterms corresponding to the value 1 of the function.
So, we can see that:
DCF(f) = m0 ∨ m3 ∨ m4 ∨ m5 ∨ m7 ∨ m8 ∨ m11 ∨ m12 ∨ m15
Or,
DCF(f) = a0b0c0d0 ∨ a0b0c1d1 ∨ a0b1c0d0 ∨ a0b1c0d1 ∨ a0b1c1d1 ∨ a1b0c0d0 ∨ a1b0c1d1 ∨ a1b1c0d0 ∨ a1b1c1d1
DCF(f) = a̅ b̅ c̅ d̅ ∨ a̅ b̅ c d ∨ a̅ b c̅ d̅ ∨
a̅ b c̅ d ∨ a̅ b c d ∨ a b̅ c̅ d̅ ∨ a b̅ c d ∨
a b c̅ d̅ ∨ a b c d

## Slide 6: Placing the minterms in a Veitch diagram
DCF(f) = m0 ∨ m3 ∨ m4 ∨ m5 ∨ m7 ∨ m8 ∨ m11 ∨ m12 ∨ m15
m15 |  | m5 | m7
 | m12 | m4 | 
 | m8 | m0 | 
m11 |  |  | m3
a
a̅
c̅
c
c
b
b̅
d
d̅
d

## Slide 7: Factorization
The Veitch diagram:
Two double factorizations:
max1 = m12 ∨ m4 ∨ m8 ∨ m0 = c̅ d̅
max2 = m15 ∨ m7 ∨ m11 ∨ m3 = cd
Two simple factorizations :
max3 = m5 ∨ m7 = a̅bc̅
max4 = m5 ∨ m4 = a̅bd
So, M(f) = {max1, max2, max3, max4}
DCF(f) = m0 ∨ m3 ∨ m4 ∨ m5 ∨ m7 ∨ m8 ∨ m11 ∨ m12 ∨ m15

## Slide 8: Simplification of the function
The Veitch diagram:
max1 = m12 ∨ m4 ∨ m8 ∨ m0 = c̅ d̅
max2 = m15 ∨ m7 ∨ m11 ∨ m3 = cd
max3 = m5 ∨ m7 = a̅bc̅
max4 = m5 ∨ m4 = a̅bd
M(f) = {max1, max2, max3, max4}
C(f) = {max1, max2}
M(f) ≠ C(f) and C(f) ≠ ∅, so we are in the second case of the simplification algorithm
We denote by g = max1 ∨ max2
g = c̅ d̅ ∨ cd
We obtain two simplified forms of f:
fS1 = g ∨ max3 = c̅ d̅ ∨ cd ∨ a̅bc̅
fS2 = g ∨ max4 = c̅ d̅ ∨ cd ∨ a̅bd

## Slide 9: Logic circuits

## Slide 10: First circuit
fS1 = c̅ d̅ ∨ cd ∨ a̅bc̅

## Slide 11: Second circuit
fS2 = c̅ d̅ ∨ cd ∨ a̅bd

## Slide 12
Thank you for your attention!